## Slide 1: System Analysis Advisory Committee - A New Metric -
Michael Schilmoeller
Tuesday, September 27, 2011

## Slide 2: Why Consider a New Metric?
We have observed that decision makers tend to emphasize least-risk plans
The choice of least-risk plans is strongly (exclusively?) influenced by a handful of futures. About 70 of the 75 “worst” (highest-cost) futures are common among all the plans on the efficient frontier
The costs in these futures is largely determined by the higher loads in these futures
Is it appropriate that least-risk plans are strongly influenced by high-load futures?

## Slide 3: What’s the Difference?
If there is only a single, fixed load forecast, there isn’t any difference: a plan that provides for minimum cost for the Region provides minimum unit energy cost.
However, if loads vary from future to future, there may be a significant difference

## Slide 4: A Few Key Points
Loads are “frozen efficiency” loads
  Loads changes therefore do not correspond to any energy efficiency improvements or changes
A unit energy cost (¢/kWh) is NOT a utility rate (¢/kWh)

## Slide 5: Frozen Efficiency Loads
The loads in the RPM are what we refer to as “frozen efficiency loads”
Because we want to consider all sources of conservation as resources, we use a load forecast that assumes:
  Discontinuation of utility conservation programs
  No new appliance standards
  No new building codes
  No electricity price-induced conservation
They do include transmission and distribution losses
Candidate conservation shows up on the resource side of the ledger: we treat its cost and energy like any other future resource

## Slide 6: Load Futures
Changes in loads among futures have nothing to do changes in conservation policy
One way to think of load futures is in terms of households and businesses moving into or out of the region, rather than changes in usage by individual customers
It is also true that individual customers may buy more or fewer gadgets and require more electricity
What is true in any of these situations, however, is that individual regional customer satisfaction will track their unit energy cost, irrespective of whether their requirements are met through energy efficiency or purchases of electricity from their utility

## Slide 7: Unit Energy Cost ≠ Rates
Costs in the rate numerator include embedded costs; costs in unit energy cost do not
Energy in the rate denominator is sales; energy in the unit energy cost is frozen efficiency load, including system losses

## Slide 8: Start with the Cash Flows

## Slide 9: Calculating NPV for One Future (discount rate = 4%)
NPV = $227.1 B

## Slide 10: Calculating NPV Cost per MWh for One Future
NPV/MWh = $1,017.03

## Slide 11: Second Future: Lower Loads

## Slide 12: Thinking of Load Growth in Terms of More Customers

## Slide 13: Reduced Load in Terms of Fewer Customers …

## Slide 14: Costs are Also Lower….

## Slide 15: … And Costs Are Distributed Over Fewer Units of Energy
Higher load future: 29,571 MWa
Lower load future: 25,428 MWa
Difference: 4,143 MWa (-14 %)
Higher load future cost: $23.5 B
Lower load future cost: $21.5 B
Difference: $2.0 B (-8.5 %)
While cost in the last year goes down 8.5 percent, cost per kWh increases by 6.4 percent !

## Slide 16: Is This Future Better or Worse Than the First Future?
Is it a bad outcome if all customers see higher bills because regional loads have fallen more than regional cost?
Is it a bad outcome for all customers to see lower bills although total regional costs are higher?
As we currently measure cost and risk, the first is a good outcome and the second is a bad outcome.

## Slide 17: While You Consider The Previous Questions …
How would the new calculation be incorporated into RPM resource choice?
What are the likely consequences of the new metric?
What are the differences between this and a rate calculation?

## Slide 18: The Existing Distribution
C:\Documents and Settings\Michael Schilmoeller\Desktop\NWPCC - Council\SAAC\Presentation materials\L813 NPV Costs.xlsm

## Slide 19: 1. Use of the New Observations
We get a distribution with a little different shape and a much different scale
We would calculate the expected cost and risk measures exactly as before but would apply them to the new “observations”

## Slide 20: The New Distribution
The first future we just examined is probably counted in this bin

## Slide 21: 2. There is a Difference in Plans on the Efficient Frontier
We ran the same model twice, but optimized the plan selection and creation of the efficient frontier using the two metrics
Both model runs produce both metrics for cost and risk for each plan
We identified the plans on efficient frontier with respect to the new load-normalized NPV metric
Using the traditional NPV metric values for these plans, we plotted them on the feasibility space with traditional coordinates

## Slide 22: What do Plans Selected Using the Modified Metric Look Like?

## Slide 23: Differences between the Least-Risk Plans
Because high-load futures play a less prominent role in the selection of resources, we would expect to see less resource capacity optioned

## Slide 24: Differences between the Least-Risk Plans
The effect on conservation targets, CO2 produced, and rate variation is minimal, however (e.g., conservation drops 184MWa)
With fewer new, cleaner turbines, CO2 production increases slightly

## Slide 25: Conclusions
This metric provides an alternative concept of “bad” – or risky – and “good” futures.
The new metric
  Is simply the application of the existing statistical measures to new values for the observations
  Will result in different least-risk plans, probably with less capacity and conservation optioned
This metric would be added to the existing metrics, not replace them

## Slide 26: Final Observation
The cost per unit energy metric is not a surrogate for utility rates
Rates are calculated differently!
  The energy value appearing in the denominator of a rate calculation is sales; it is reduced by conservation energy and T&D losses
  Cost of conservation often is expensed
We know that using rates as an objective does not guarantee lowest total resource cost; TRC is in fact likely to be higher

## Slide 27: End